## Slide 1
CENG 4100 · COMPUTER ARCHITECTURE
Week 1
Meet the Machine
Phase 0 — Baseline · Milestone M0 begins
DUNWOODY
COLLEGE OF TECHNOLOGY

## Slide 2
This Week | Meet the Machine
You inherit a working RISC-V processor and spend the whole semester growing it. Today: meet the tools, meet the core, and put a design on real hardware.
Concept
What computer architecture is, the levels of abstraction from transistors to programs, and the RV32I base core you'll evolve for 16 weeks.
Read: SCO Ch 1; COD 1.1–1.5
Lab
Install Vivado, open the base-core project, and program the Basys 3 (Artix-7). Read the RTL top module top to bottom and annotate it.
Deliverable
A running demo bitstream on your board + a one-page RTL map in your design notebook.
One core, all semester: everything you build from here bolts onto the design you meet today.
D
1

## Slide 3
Levels of Abstraction | The Stack
A modern computer is a stack of layers. Architecture is the contract between the hardware and the software — the layer this course lives in.
1
APPLICATION
Your C or assembly program — what you want the machine to do.
2
ISA
The instruction set: the visible contract. We use RISC-V (RV32I).
3
MICROARCH.
How the ISA is actually built: datapath, control, pipeline.
4
LOGIC / RTL
Gates, registers, and FSMs written in Verilog.
5
FPGA
LUTs and flip-flops on the Artix-7 that become your circuit.
Architecture (the ISA) is the promise; microarchitecture is how you keep it. This course crosses both.
D
2

## Slide 4
The Toolchain | Vivado + Basys 3
Two things you'll use every week: Vivado turns your Verilog into a bitstream, and the Basys 3 runs it as real silicon.
TODAY'S SETUP
1
Install Vivado. Free Standard edition; add the Artix-7 (7-series) device family.
2
Open the base core. Load the provided project; set the Basys 3 xc7a35tcpg236-1 as the target part.
3
Synthesize & implement. Run synthesis → implementation → generate bitstream.
4
Program the board. Open Hardware Manager, connect over USB-JTAG, program the device.
BASYS 3 · ARTIX-7 xc7a35tcpg236-1
33,280 logic cells · 5,200 slices (4 LUTs + 8 FFs each)
90 DSP slices · 1,800 Kb block RAM
16 switches · 16 LEDs · 5 buttons · 4-digit 7-seg
USB-JTAG programming · USB-UART bridge · 4 Pmods
Write → Synthesize → Implement → Program. That loop never changes, all semester.
D
3

## Slide 5
Read the RTL
The base core, top to bottom
D
4

## Slide 6
The Base Core | A Single-Cycle RV32I
The core you inherit executes one instruction per clock. Five blocks do all the work — learn their names now; you'll rebuild every one.
FETCH
PC register
Instruction memory
PC + 4 adder
DECODE
Register file (32×32)
Immediate generator
Control unit
EXECUTE
ALU
ALU control
Branch compare
MEM / WB
Data memory
Load/store logic
Write-back mux
rv_top.v
1
module rv_top(input clk, input rst,
2
output [15:0] led);
3
wire [31:0] pc, instr, alu_y, rdata;
4
fetch u_if (.clk(clk), .rst(rst), .pc(pc), .instr(instr));
5
decode u_id (.instr(instr), .imm(imm), .ctrl(ctrl));
6
execute u_ex(.a(rs1), .b(rs2), .imm(imm), .y(alu_y));
7
endmodule
D
5

## Slide 7
How to Read RTL | Follow the Signals
Don't read Verilog top to bottom like a novel. Follow one signal — the program counter — as it flows through the design.
1
Find the clock & reset. Every sequential block keys off posedge clk and rst.
2
Find the PC register. It's the heartbeat — where does it get its next value?
3
Trace instruction fetch. PC indexes instruction memory → the 32-bit instr word.
4
Watch it split in decode. Opcode, funct3/7, register fields, immediate.
5
Follow to write-back. Where does the result land back in the register file?
VIVADO TCL CONSOLE
$ open_project rv_core.xpr
$ launch_runs synth_1
INFO: synthesis complete
$ launch_runs impl_1 -to_step
write_bitstream
INFO: bitstream written:
rv_top.bit
$ program device
INFO: Programmed XC7A35T
You can't change what you can't trace. Name every wire before you touch one.
D
6

## Slide 8
Working Towards Milestone M0
Meet the machine — get it running
D
7

## Slide 9
The Lab | Four Sections, One Rule
Every weekly lab has the same four sections. Work them in order — you must be able to EXPLAIN every line you submit.
1
ANCHOR
Program the provided demo to the board. Confirm your toolchain works end to end.
2
GUIDED
Annotate rv_top.v: label each of the five blocks and the signals between them.
3
EXTENSION
Change which switches drive the LEDs; re-synthesize and re-program.
4
STRETCH
Record Fmax and LUT/FF counts from the reports.
Together in class: Anchor + Guided. On your own: Extension + Stretch.
D
8

## Slide 10
Reading Response #1 | SCO Ch 1 · COD 1
Reading responses are 15% of your grade. Short, specific answers in your own words — post to Canvas before next class.
DEFINE
What is the difference between computer ARCHITECTURE and ORGANIZATION?
Name the six levels in Tanenbaum's layered machine.
EXPLAIN
Why is the ISA called a 'contract'? Who are the two parties?
What does 'RISC' mean, and what does the 'V' add?
APPLY
List the five blocks of the base core and one job each.
Which Basys 3 resources limit how big your core can grow?
D
9

## Slide 11
Week 1 Reflection | Design Notebook
Close every week here. Log it in your design notebook — the notebook + check-ins are 8% of your grade.
D
10

## Slide 12
By December, this goes on your résumé
Built and deployed a working RISC-V (RV32I) processor in Verilog on a Xilinx Artix-7 FPGA including datapath, control, pipelining, and cache using Vivado, IP Integrator, and RTL simulation.
D
10
RISC-V Processor Design & FPGA Implementation
Designed and built a working single-cycle RISC-V (RV32I) processor from the ground up in Verilog, progressing from combinational logic to a complete stored-program computer, and deployed it to a Xilinx Artix-7 FPGA (Digilent Basys 3).
Constructed the full datapath block-by-block in Vivado IP Integrator — ALU, register file, program counter, instruction decoder, and write-back logic — validating each stage in simulation and on hardware.
Extended the processor incrementally: added new ALU operations and a custom instruction (decode → ALU-control → datapath), an RV32M multiply/divide unit, a 5-stage pipeline with hazard detection and forwarding, and a data cache.*
Verified designs with Verilog testbenches (Icarus Verilog/Vivado XSim); closed timing at 100 MHz and analyzed LUT/FF/DSP utilization and Fmax against the iron law of performance (IC × CPI × T).
Contrasted CISC vs. RISC by microcoding an instruction on a Mic-1/IJVM model, then implementing the same operation as hardwired RISC logic.
Skills
Hardware / FPGA: Verilog RTL, Vivado Design Suite, IP Integrator (block design), Xilinx Artix-7 / Basys 3, XDC timing & pin constraints, RTL simulation (XSim/Icarus), timing closure, synthesis & utilization analysis Computer Architecture: RISC-V (RV32I/RV32M), single-cycle & pipelined datapath design, hazard/forwarding, instruction decode & control, ALU design, register files, memory hierarchy/caches, CISC microcode (Mic-1/IJVM) Concepts: digital logic design, combinational vs. sequential logic, clocking & FSMs, performance analysis (CPI, Fmax, AMAT)