## Slide 1
CENG 4100 · COMPUTER ARCHITECTURE
Week 2
Measure It
Phase 0 — Baseline · Milestone M0 completes
DUNWOODY
COLLEGE OF TECHNOLOGY

## Slide 2
This Week | Measure It
You can't improve what you don't measure. Today you pin down the numbers that define your baseline — and that every later change will be judged against.
Concept
The performance equation, CPI, clock rate vs. Fmax, FPGA utilization, and Amdahl's law.
Read: COD 1.6–1.12; SCO 2.1
Lab · M0
Run a reference program on the core. Record the baseline: cycle count, Fmax, and LUT / FF / BRAM / DSP utilization.
Deliverable
A baseline table in your design notebook. These numbers are the 'before' for the whole semester. Reading response #2.
Today's numbers are the yardstick. Every optimization from here gets measured against them.
D
1

## Slide 3
Where We Are | The Core Runs
Last week you met the machine and put it on the board. Now we quantify exactly what 'it runs' means.
1
DONE · W1
Vivado installed, base core programmed to the Basys 3.
2
DONE · W1
Read the RTL top to bottom; named all five blocks.
3
TODAY
Measure cycles, Fmax, and utilization — lock the baseline.
4
NEXT · W3
Start changing the hardware: add an instruction.
Milestone M0 = a running core you fully understand and have measured. Finish it today.
D
2

## Slide 4
Performance | The One Equation
All of processor performance reduces to one equation. Everything you build this semester moves one of its three terms.
CPU time = Instructions × CPI × Clock period
IC
Instruction count — set by the ISA and the compiler.
CPI
Cycles per instruction — set by the microarchitecture.
T
Clock period (1 / Fmax) — set by the critical path.
Lower any one factor without raising the others, and the program runs faster. That's the whole game.
D
3

## Slide 5
Three Levers | Who Controls What
Each term has a different owner. Knowing who controls each keeps you from 'optimizing' something you can't actually move.
INSTRUCTION COUNT
Owned by the ISA + compiler
A richer instruction can do more per line (CISC)
You'll change this in Week 5 by adding an instruction
CPI
Owned by the microarchitecture
Single-cycle = 1, but forces a slow clock
Pipelining (Week 7+) attacks this — ideally toward 1 at high clock
CLOCK PERIOD
Owned by the critical path
= 1 / Fmax, reported by Vivado timing
Shorter logic between registers → higher Fmax
Beware the trap: single-cycle wins on CPI but loses on clock period. Net speed is the product.
D
4

## Slide 6
Timing | Fmax & the Critical Path
On an FPGA your clock speed isn't a spec — it's an outcome. Vivado computes the longest logic delay and tells you how fast you may run.
1
Critical path. The slowest register-to-register logic delay in the design.
2
Setup slack (WNS). Time to spare before the next clock edge. Negative = fails timing.
3
Fmax. The highest clock the design can meet: 1 / (T − WNS).
4
Your job. Shorten the critical path to raise Fmax — without breaking correctness.
TIMING SUMMARY
$ report_timing_summary
Design Timing Summary
WNS(ns) TNS(ns)
------- --------
1.24 0.000
All user constraints met.
Clock: sys_clk 100.00 MHz
Fmax ~= 1/(10ns-1.24ns)
~= 114 MHz
Positive slack means you have headroom. Negative slack means the design is lying about its clock.
D
5

## Slide 7
Utilization | The Artix-7 Budget
Your core is carved out of finite silicon. The Basys 3's XC7A35T gives you a fixed budget of four resource types.
20,800
LUTs — logic (33,280 cells / 5,200 slices)
41,600
Flip-flops — state and pipeline registers
50
36Kb BRAMs — 1,800 Kb of block RAM
90
DSP48 slices — fast multiply / MAC
Watch the DSP and BRAM counts especially — a multiplier or a cache can exhaust them fast.
D
6

## Slide 8
Code-Along | Read the Reports
The two reports you'll open every week. Run them after implementation and copy the numbers straight into your notebook.
UTILIZATION REPORT
$ report_utilization
+----------------+------+-------+
| Site Type | Used | Avail |
+----------------+------+-------+
| Slice LUTs | 1842 | 20800 |
| Slice Registers| 987 | 41600 |
| Block RAM Tile | 2 | 50 |
| DSPs | 0 | 90 |
+----------------+------+-------+
BASELINE TO RECORD
Cycle count for the reference program (from simulation)
Fmax from the timing summary (1 / (T − WNS))
LUT / FF / BRAM / DSP counts from utilization
CPI = cycles ÷ instructions retired
Six numbers. Write them down once; you'll compare against them for fifteen weeks.
D
7

## Slide 9
Amdahl's Law | The Reality Check
Before you optimize anything, ask how much it can possibly help. Amdahl's law caps your speedup by the fraction you actually touch.
Speedup = 1 / ( (1 − f) + f / s )
F = FRACTION AFFECTED
Speed up 30% of runtime → best case is a 1.43× overall, ever.
S = LOCAL SPEEDUP
Make that 30% infinitely fast (s→∞) → still only 1 / 0.7 = 1.43×.
THE LESSON
Optimize the common case. A huge win on a rare path barely moves the needle.
Make the common case fast. Amdahl decides whether an optimization is worth the effort.
D
8

## Slide 10
Milestone M0 · Lab
Measure it — lock the baseline
D
9

## Slide 11
The Lab | Record the Baseline
Run the reference program and capture six numbers. Same four sections, same rule: explain every value you report.
1
ANCHOR
Simulate the reference program; read the retired-instruction and cycle counts.
2
GUIDED
Implement the design; pull Fmax from timing and LUT/FF/BRAM/DSP from utilization.
3
EXTENSION
Compute CPI and CPU time. Fill in the baseline table.
4
STRETCH
Predict which single change would help most — and cite Amdahl. (Optional.)
Together in class: Anchor + Guided. On your own: Extension + Stretch.
D
10

## Slide 12
Reading Response #2 | COD 1.6–1.12
Short, specific, in your own words. Post to Canvas before next class.
DEFINE
Write the performance equation and name each term's owner.
What is the difference between clock RATE and Fmax?
EXPLAIN
Why can a lower CPI still mean a SLOWER processor?
What does negative setup slack (WNS) actually mean?
APPLY
Given IC, CPI, and Fmax, compute CPU time.
Use Amdahl to bound a speedup on 40% of runtime.
Show the arithmetic. A number without units earns no credit.
D
11

## Slide 13
Week 2 Reflection | Design Notebook
Log your baseline and your reasoning. Notebook + check-ins are 8% of your grade.
1
State your baseline: cycles, IC, CPI, Fmax, and the four utilization numbers.
2
Explain the trade: why does single-cycle give CPI = 1 but a low Fmax?
3
Predict: which resource (LUT/FF/BRAM/DSP) will run out first as you grow the core?
4
One question: which report number surprised you most, and why?
Next week → Add an instruction: meet the single-cycle datapath you're about to edit.
D
12