## Slide 1
COMPUTER ARCHITECTURE · RISC-V: FPGA TO SILICON
Week 2
Trace Before You Modify
DUNWOODY
COLLEGE OF TECHNOLOGY

## Slide 2
Where we left off
The core runs
A complete single-cycle RV32I works on the Basys 3 and passes a self-checking simulation.
But do you understand it?
Running code you didn’t write is not the same as knowing how it works inside.
This week
Trace the core by hand, prove you understand it, then add your first instruction.
The gate
A lockstep harness checks every change against a golden model — no change ships unverified.
D
2

## Slide 3
Why Trace Before Modify
Brownfield — starting from working code — is the right way to learn ISA extension. But it has one failure mode.
THE RISK
Cargo-culting
Copy-paste changes until the test passes, with no real understanding. The code works but you didn’t learn.
The fix
Before touching the RTL, prove you can trace one instruction through the datapath by hand.
Adding an instruction is self-validating — you can’t do it without understanding decode, datapath, and control.
THE GATE
1
Pick an instruction — choose one the core already runs.
2
Trace it — follow it through fetch, decode, register read, ALU, and writeback.
3
Diff against the model — compare your trace to a golden ISA simulator’s.
4
Only then extend — once it matches, you’ve earned the right to modify the RTL.
Comprehension first, code second.
D
3

## Slide 4
How to Trace an Instruction
Tracing means following one instruction through the datapath, predicting the value on every wire, then confirming against the hardware.
WHAT YOU’RE DOING
Predict, then check
Work out each signal by hand first — don’t peek at the simulator until you’ve committed to an answer.
Every wire, in order
PC, instruction word, decoded fields, control bits, register reads, ALU, writeback, next PC.
If your prediction matches the hardware on every signal, you understand that instruction’s path.
THE METHOD
1
Locate the cycle — find the PC where your instruction runs (e.g. PC = 0x08).
2
Decode the word — split the 32-bit instruction into op, rd, rs1, rs2, funct.
3
Predict control — regwrite, ALU source, ALU op, result source, branch / jump.
4
Predict the datapath — register reads, ALU inputs, ALU output, the writeback value.
5
Confirm — read the signals in GTKWave, or peek them in cocotb, and compare.
Predict on paper, confirm in simulation. The gap between the two is exactly what you don’t yet understand.
D
4

## Slide 5
Worked Trace | add x3, x1, x2
At PC 0x08 the core runs add x3, x1, x2, with x1 = 5 and x2 = 10. Here is every signal, predicted by hand.
DECODE THE WORD
instr = 0x002081b3
Field | Bits | Means
op | 0110011 | R-type
rd | 00011 | x3
rs1 | 00001 | x1
rs2 | 00010 | x2
funct3 | 000 | add
FOLLOW THE SIGNALS
Stage | Value
register reads rd1, rd2 | 5, 10
ALU control | ADD (4'd0)
ALU inputs srcA, srcB | 5, 10
ALU result | 15
writeback | x3 <= 15
next PC | 0x0C
Predicted: x3 = 15, next PC = 0x0C. Run it and the signals match — you’ve traced the whole R-type path.
D
5

## Slide 6
The Lockstep Idea | RTL vs Golden Model
Run two implementations of RV32I side by side — your hardware and a trusted reference — and compare them every instruction.
TWO MODELS, ONE TRUTH
The RTL core
Your Verilog processor, simulated cycle by cycle. This is the thing under test.
The golden model
A small, readable RV32I interpreter (or Spike) that defines correct behavior.
If they ever disagree, the RTL is wrong — and you find out at the exact instruction.
EVERY INSTRUCTION, COMPARE:
1
PC — the address of the instruction that just ran.
2
Register write — which register changed, and to what value.
3
Memory store — which address was written, and with what data.
Three things pin RV32I behavior down completely. Match all three and the cores agree.
D
6

## Slide 7
What Lockstep Does Each Cycle
One instruction retires per clock in the single-cycle core, so the harness steps both models together.
1
SAMPLE RTL
Read the core’s PC, register writeback, and any store this cycle.
2
STEP MODEL
Advance the golden model by exactly one instruction.
3
COMPARE
Check that PC, writeback, and store all match between the two.
4
REPORT
On the first mismatch, print the PC and both values — then stop.
The first divergence is the bug. No guessing, no waveform archaeology.
D
7

## Slide 8
Run the Harness
From “it compiles” to “it’s correct”
D
8

## Slide 9
Run Lockstep | Core vs Golden Model
Assemble a coverage program, then run the RTL and the model in lockstep.
1
Assemble a program — make prog turns assembly into a hex image the core loads.
2
Run the harness — make sim simulates the core and steps the model alongside it.
3
Every instruction checked — PC, register writes, and stores compared automatically.
4
Read the result — a clean run reports how many instructions matched.
test_lockstep.py
1
make prog && make sim
2
RTL vs golden ISS
TERMINAL
lockstep OK: 37 instructions
matched, halt at 0x0000_00b0
** test_lockstep PASS
37 instructions — every R-type, branch, jump, load and store — matched exactly.
D
9

## Slide 10
It Catches Real Bugs | A Deliberate Fault
A gate is only worth trusting if it fails when the design is wrong. So break something on purpose.
1
Inject a fault — make the ALU compute a + b where it should compute a − b.
2
Re-run lockstep — the same harness, with no other changes.
3
First divergence flagged — the harness stops at the exact instruction.
4
Read the report — the PC, the wrong value, and the right value.
alu.v (sub broken)
1
4'd1: y = a + b; // was a-b
TERMINAL
[3] @pc 0x0000_000c
writeback mismatch:
rtl(x4<=107)
iss(x4<=93)
** test_lockstep FAIL
sub gave 100 + 7 = 107 instead of 100 − 7 = 93 — caught at the exact PC. You can’t pass by accident.
D
10

## Slide 11
Your First Extension | Three Touch Points
Adding an instruction to this core touches a small, predictable set of places — and nothing else.
1
DECODE
Map the new opcode to control signals in the main decoder.
2
ALU CONTROL
Map it to an ALU operation in the alu decoder.
3
ALU
Implement the operation itself.
You can’t place these three edits correctly without understanding how decode, control, and datapath connect. That’s the point.
D
11

## Slide 12
Add an Instruction | popcount, in Three Edits
A custom popcount (count set bits) instruction, added in three edits and verified against the model.
1
Choose an encoding — use the RISC-V custom-0 opcode, an R-type style layout.
2
Decode it — add one line to the main decoder for the new opcode.
3
Wire the ALU — add an ALU-control code and the popcount operation.
4
Verify it — a lockstep test checks it against a Python reference.
three edits
1
// main_decoder.v
2
7'b0001011: begin
3
regwrite=1; aluop=2'd3;
4
end
5
// alu_decoder.v
6
2'd3: aluctrl = 4'd10;
7
// alu.v
8
4'd10: y = popcount(a);
TERMINAL
lockstep OK: pcnt verified
Three edits, one new instruction — and the harness proves it’s right before you trust it.
D
12

## Slide 13
How to Verify an Instruction
Tracing proves you understand it. Verification proves it’s correct — automatically, for every input, not just the one you traced.
WHERE TRUTH COMES FROM
Existing instructions
Spike or the bundled golden ISS already defines correct RV32I behavior — lockstep against it.
Custom instructions
The reference doesn’t know your new op. Teach the model the behavior, or check an independent oracle.
The core is never its own judge. “Correct” means: agrees with a reference you trust.
THREE LAYERS
1
Directed — a program that hits the instruction on hand-picked inputs — zero, all-ones, edges.
2
Differential — lockstep every instruction’s result against the golden model.
3
Randomized — thousands of random inputs; any single divergence is a real bug.
Directed catches the obvious; random catches what you didn’t think of.
D
13

## Slide 14
Verify popcount | The Idea
An oracle is a trusted second opinion. Compare the core’s answer to it on many inputs — if they ever differ, the core is wrong.
1
Define an oracle — a trusted way to get the right answer, independent of the core.
2
Drive the core — give it an input and run the new instruction.
3
Compare — check the core’s result against the oracle’s.
4
Repeat at scale — a thousand random inputs, every one checked.
pseudocode
1
oracle(x) = count of 1-bits in x
2
3
repeat 1000 times:
4
x = a random 32-bit value
5
run pcnt on x in the core
6
check result == oracle(x)
IDEA
oracle = trusted answer
any mismatch = a real bug
The oracle is the truth; the loop is the search. Random inputs find what you’d never think to test.
D
14

## Slide 15
Code Along | Verify popcount for Real
Two one-line edits finish the loop: teach the golden model what popcount means, and teach the assembler how to encode it. The harness does the rest.
1
Teach the model — one line in the golden ISS, mirroring your RTL edit.
2
Teach the assembler — one line so pcnt rd, rs1 encodes to the custom-0 opcode.
3
Run lockstep — make prog && make sim — no new test to write.
4
Read PASS — every instruction, pcnt included, checked against the model.
model + assembler
1
# golden model - rv32i_iss.py
2
elif op == 0x0B:
3
wb(bin(a).count("1"))
4
# assembler - asm.py
5
if op == "pcnt": out.append(
6
enc_i(reg(args[0]), reg(args[1]),
7
0, 0, op=0x0B))
TERMINAL
$ make prog && make sim
lockstep OK: pcnt verified
Validated: pcnt x2, x1 on 0xFF gives 8 — RTL and model agree, lockstep PASS. Nothing left implied.
D
15

## Slide 16
Understand → Extend → Verify
You traced the core, ran it in lockstep against a golden model, proved the gate catches bugs, and added your first instruction.
1
UNDERSTAND
Trace an instruction by hand and diff it against the reference model.
2
EXTEND
Add an instruction in three predictable edits: decode, ALU control, ALU.
3
VERIFY
Lockstep plus an oracle proves every change against a reference — automatically.
Next: sub-word memory and a multicycle multiply — extensions that reshape the datapath itself.
D
16