## Slide 1
CENG 4100 · COMPUTER ARCHITECTURE
Week 3
Add an Instruction
Phase 1 — The ISA · Milestone M1 begins
DUNWOODY
COLLEGE OF TECHNOLOGY

## Slide 2
This Week | Know the Datapath
Before you edit a processor you must be able to trace it. This week is a logic refresher plus a full tour of the single-cycle datapath and control you're about to change.
Concept
Digital-logic refresher, RISC-V instruction formats, and the single-cycle datapath + control.
Read: SCO 3.1–3.3; COD App. A; COD 4.1–4.4
Lab · M1
Study the datapath and control you'll edit. Trace one instruction end to end and mark exactly where a new one would plug in.
Deliverable
An annotated datapath diagram + a list of edit points for your assigned instruction. Reading response #3.
This week you don't build — you map. Next week you start cutting.
D
1

## Slide 3
Where We Are | Baseline Locked
Phase 0 is done: a measured, understood core. Phase 1 begins — you'll add one instruction two ways, first in microcode, then in hardware.
1
DONE · P0
Core runs on the board; baseline cycles, Fmax, and utilization recorded.
2
TODAY
Study the single-cycle datapath and control; refresh your logic.
3
NEXT · W4
Add the instruction the CISC way — Mic-1 microcode.
4
THEN · W5
Add it the RISC way — real hardware in the core.
Milestone M1 spans three weeks: understand it, microcode it, then build it in hardware.
D
2

## Slide 4
Logic Refresher | The Building Blocks
Every datapath is made of four kinds of block. If these feel rusty, review COD Appendix A before the lab.
Gates & Mux
AND / OR / XOR / NOT and the multiplexer — the mux is how the datapath 'chooses' a source each cycle.
Adder / ALU
Ripple-carry adder, then a full ALU: add, subtract, AND, OR, shifts, and set-less-than.
Registers
Edge-triggered flip-flops. The PC and the 32×32 register file are just banks of these.
FSMs
State + next-state logic. Control is a (tiny) FSM; multicycle machines are bigger ones.
Combinational logic computes; sequential logic remembers. A datapath is both, wired together.
D
3

## Slide 5
Comb. vs Seq. | Two Kinds of always
In Verilog, the block style encodes the timing. Get this right and the synthesizer builds what you meant.
styles.v
1
// combinational: no memory
2
always @(*)
3
y = sel ? a : b; // a mux
4
5
// sequential: edge-triggered
6
always @(posedge clk)
7
if (rst) q <= 0;
8
else q <= d; // a register
COMBINATIONAL
Output follows input, no clock — use always @(*)
Blocking =. Builds muxes, ALUs, decoders
SEQUENTIAL
Updates on the clock edge — always @(posedge clk)
Non-blocking <=. Builds PC, regfile, pipeline regs
Combinational = ; sequential <=. Mixing them is the #1 source of surprise synthesis bugs.
D
4

## Slide 6
RISC-V Formats | Six Shapes
Every RV32I instruction is 32 bits in one of six formats. The format decides which fields the decoder pulls out.
R-type
reg-reg: add, sub, and. funct7 · rs2 · rs1 · funct3 · rd.
I-type
imm & loads: addi, lw, jalr. 12-bit signed immediate.
S-type
stores: sw. Immediate split across two fields.
B-type
branches: beq, bne. 13-bit imm, low bit implied 0.
U-type
upper imm: lui, auipc. 20-bit imm into the high bits.
J-type
jumps: jal. 21-bit signed target offset.
Learn where rd, rs1, rs2, and the immediate live in each — the decoder is just field extraction.
D
5

## Slide 7
The Datapath | One Instruction, One Clock
Follow an add instruction left to right. In a single-cycle machine, all five stages happen within one clock period.
1
FETCH
PC addresses instruction memory; PC+4 computed for next cycle.
2
DECODE
Fields split out; register file reads rs1, rs2; control decodes opcode.
3
EXECUTE
ALU computes rs1 (op) rs2, or rs1 + immediate.
4
MEMORY
Loads/stores access data memory; others pass through.
5
WRITE-BACK
Result mux picks ALU / memory / PC+4 into rd.
Everything is combinational except the PC and register-file writes. That's why it fits in one cycle.
D
6

## Slide 8
The Control Unit | Opcode → Signals
Control is a lookup: the opcode (and funct fields) map to the mux selects and enables that steer the datapath.
control.v
1
always @(*) case (opcode)
2
7'b0110011: begin // R-type
3
reg_write = 1;
4
alu_src = 0; // rs2
5
mem_to_reg= 0;
6
end
7
7'b0000011: begin // load
8
reg_write = 1;
9
alu_src = 1; // imm
10
mem_read = 1;
11
end
12
endcase
SIGNALS TO KNOW
reg_write — does the instruction write rd?
alu_src — second ALU input: register or immediate?
mem_read / mem_write — touch data memory?
mem_to_reg — write-back from ALU or memory?
branch — is the PC redirected on a condition?
Adding an instruction = teaching this case statement one new row, and maybe teaching the ALU one new op.
D
7

## Slide 9
Milestone M1 · Lab
Study the datapath you'll edit
D
8

## Slide 10
The Lab | Trace & Mark
No edits yet — just deep understanding. Trace your assigned instruction and mark every place it will need to touch.
1
ANCHOR
Trace an add through the datapath; list every signal it sets.
2
GUIDED
Annotate the datapath diagram: label muxes, control signals, and enables.
3
EXTENSION
For your assigned instruction, identify its format and required control signals.
4
STRETCH
Sketch the exact RTL edits you'd make — decode, ALU, mux. (Optional.)
Together in class: Anchor + Guided. On your own: Extension + Stretch.
D
9

## Slide 11
Reading Response #3 | COD 4.1–4.4
Short, specific, in your own words. Post to Canvas before next class.
DEFINE
Name the five datapath stages and one job each.
What is the difference between blocking and non-blocking assignment?
EXPLAIN
Why is the single-cycle clock period set by the SLOWEST instruction?
What does the alu_src mux choose between?
APPLY
Identify the format of your assigned instruction.
List the control signals it must assert.
Tie every answer back to a signal or a stage you could point to in the RTL.
D
10

## Slide 12
Week 3 Reflection | Design Notebook
Capture your datapath map and edit plan. Notebook + check-ins are 8% of your grade.
1
In your own words: why does everything fit in one clock in a single-cycle core?
2
Trace it: write the signal path of one instruction from PC to write-back.
3
Plan the edit: name the RTL blocks your assigned instruction will change.
4
One question: which control signal's purpose is still fuzzy? Bring it to office hours.
Next week → Add it the CISC way: extend the Mic-1 microcode with your instruction.
D
11