## Slide 1
COMPUTER ARCHITECTURE · RISC-V: FPGA TO SILICON
Week 3
Sub-Word Memory: Bytes, Halfwords & Lanes
DUNWOODY
COLLEGE OF TECHNOLOGY

## Slide 2
Where we left off
The core extends cleanly
You added a custom instruction in five small edits, verified end-to-end by lockstep.
But access is coarse
The core only moves whole 32-bit words — lw and sw. Nothing finer.
Real programs need bytes
Characters, booleans, and packed protocol fields live one byte at a time.
This week
Add lb / lh / lbu / lhu / sb / sh — the first extension that reshapes the datapath.
D
2

## Slide 3
Why Sub-Word Access
Memory is byte-addressable, but the core reads and writes a full word at a time. Characters, flags, and packed fields need finer access.
WHY IT MATTERS
A char is one byte
A string is bytes packed four to a word; lw can't pull out a single character.
Writes must be surgical
Setting one byte must not clobber the three sitting beside it in the same word.
Byte-addressable memory, word-sized datapath — sub-word access bridges the two.
THE SIX INSTRUCTIONS
1
lb / lh — load byte / halfword, sign-extended to 32 bits.
2
lbu / lhu — load byte / halfword, zero-extended.
3
sb / sh — store the low byte / halfword of a register.
4
lw / sw — the word forms you already have.
Same opcodes as lw/sw — funct3 picks the width, so the decoder already routes them.
D
3

## Slide 4
Three Problems
Three mechanisms, and nothing else, separate lw/sw from the full sub-word set.
1
LANES
addr[1:0] selects which byte or halfword of the 32-bit word is in play.
2
EXTEND
A loaded byte or half must fill 32 bits — sign- or zero-extended, by funct3.
3
MASK
A byte store must merge into the word without disturbing its neighbors.
Lanes, extension, masking — learn these three and you've learned sub-word memory.
D
4

## Slide 5
Little-Endian Byte Lanes
One 32-bit word holds four bytes. Little-endian means the lowest address is the least-significant byte.
word at base = 0x8090A0B0
BYTE 3
[31:24]
0x80
base + 3
BYTE 2
[23:16]
0x90
base + 2
BYTE 1
[15:8]
0xA0
base + 1
BYTE 0
[7:0]
0xB0
base + 0
highest address
lowest address
addr[1:0] = 0,1,2,3 selects the byte lane; addr[1] alone selects the halfword.
D
5

## Slide 6
Load | Extract, then Extend
A load reads the whole word, picks the lane with addr[1:0], then extends it to 32 bits by funct3.
TWO STEPS
Extract
Shift the addressed byte or halfword down to bit 0, using addr[1:0].
Extend
Fill the upper bits — copy the sign bit (lb / lh) or pad with zeros (lbu / lhu).
Sign vs zero extension is the whole difference between lb and lbu.
WIDTH + EXTENSION BY funct3
funct3 | instr | width | extend
000 | lb | byte | sign
100 | lbu | byte | zero
001 | lh | half | sign
101 | lhu | half | zero
010 | lw | word | —
Five forms, one path: extract the lane, then choose how to fill the top bits.
D
6

## Slide 7
Store | Mask, then Merge
A word memory can't write a single byte. So a byte store becomes a read-modify-write of the whole word.
READ-MODIFY-WRITE
Read
Fetch the current word at the store address.
Merge
Replace just the target byte or halfword; keep the rest.
Write
Store the merged word back to memory.
(word & ~mask) | newbyte — the canonical masking idiom.
WORKED: sb INTO LANE 1
1
Target lane 1 — sb writes byte 1 of the addressed word.
2
Build the mask — 0x0000FF00 marks the byte to replace.
3
Clear + insert — (word & 0xFFFF00FF) | (newbyte << 8).
4
Neighbors survive — bytes 0, 2 and 3 are left untouched.
Read before you write: the three bytes you aren't storing have to come from somewhere.
D
7

## Slide 8
The Datapath Changes
Every change lives inside the CPU. The memory stays a plain word array.
1
DECODER
Unchanged — the lw/sw opcodes already route loads and stores.
2
LOAD PATH
A new extract-and-extend block between the memory read and writeback.
3
STORE PATH
A new mask-and-merge block before the memory write.
4
MEMORY
Unchanged — just zero-initialized for deterministic reads.
The opcodes already decoded, so sub-word is pure datapath — that's why it's the clean first extension.
D
8

## Slide 9
Code Along
Six instructions, all in the datapath
D
9

## Slide 10
RTL | The Load Path
Pick the lane by addr[1:0], extend by funct3, and feed the writeback mux a 32-bit value.
1
Byte offset — boff = aluresult[1:0] — the low address bits.
2
Select the lane — index the right byte/half of dmem_rdata.
3
Extend by funct3 — replicate the sign bit, or pad with zeros.
4
Feed writeback — loaddata replaces dmem_rdata in the mux.
rv32i.v (loads)
1
wire [1:0] boff = aluresult[1:0];
2
case (funct3)
3
3'b000: // lb (sign byte)
4
3'b100: // lbu (zero byte)
5
3'b001: // lh 3'b101: // lhu
6
default: loaddata = dmem_rdata;
7
endcase
ASSEMBLED
lb x2, 0(x10) -> 0x00050103
loaddata feeds resultsrc = 1, exactly where dmem_rdata used to go.
D
10

## Slide 11
RTL | The Store Path
Read the current word, splice in the new byte or halfword, and write the merged word back.
1
Read the word — dmem_rdata holds the current word at the address.
2
Pick the lane — boff selects the target byte or halfword.
3
Splice — keep the other bytes, replace only the target.
4
Write merged — storedata becomes dmem_wdata.
rv32i.v (stores)
1
case (funct3)
2
3'b000: case (boff) // sb
3
2'd1: storedata =
4
{rd[31:16],rd2[7:0],rd[7:0]};
5
3'b001: // sh
6
default: storedata = rd2; // sw
7
endcase
ASSEMBLED
sb x6, 1(x10) -> 0x006500a3
rd here is dmem_rdata — the three bytes you keep come straight from the current word.
D
11

## Slide 12
Model + Assembler
Teach the golden model the same widths and the assembler the six mnemonics — then lockstep covers them for free.
1
Model the loads — sign- or zero-extend, by funct3, in the golden ISS.
2
Model the stores — the same read-modify-write merge.
3
Add mnemonics — a funct3 table in the assembler.
4
Nothing else — the harness already compares every load and store.
rv32i_iss.py + asm.py
1
# iss - load, signed byte
2
bb = (word >> 8*off) & 0xFF
3
wb(bb-0x100 if bb & 0x80 else bb)
4
# asm - funct3 table
5
LOADS = {"lb":0,"lh":1,"lw":2,
6
"lbu":4,"lhu":5}
7
STORES = {"sb":0,"sh":1,"sw":2}
TERMINAL
model + assembler in step
The model defines what each width means; lockstep enforces that the RTL agrees.
D
12

## Slide 13
Run Lockstep | Every Form, Every Offset
One program exercises all six instructions across every byte offset and both halves. Lockstep checks each against the model.
1
Cover everything — lb/lh/lbu/lhu at each offset, sb/sh, then read back.
2
Assemble — make prog builds the hex image.
3
Run lockstep — make sim steps the core and model together.
4
Read PASS — 20 instructions, all matched.
subword_test.s
1
sw x1, 0(x10) # seed a word
2
lb x2, 0(x10) # signed byte
3
lbu x6, 0(x10) # unsigned
4
sb x6, 1(x10) # splice byte
5
sh x12, 2(x10) # splice half
6
lw x14, 0(x10) # read back
TERMINAL
$ make prog && make sim
lockstep OK: 20 matched
** test_lockstep PASS
Validated: 20 instructions, every sub-word form, RTL and model in lockstep — PASS.
D
13

## Slide 14
Lanes → Extend → Mask
Sub-word memory in three mechanisms — all in the datapath, all verified against the model.
1
LANES
addr[1:0] selects the byte or halfword within the word.
2
EXTEND
funct3 sign- or zero-extends a loaded byte or half to 32 bits.
3
MASK
stores read-modify-write so neighbors in the word survive.
Next: a custom functional unit, then the multicycle multiply — the extension that finally breaks the single-cycle assumption.
D
14