## Slide 1
CENG 4100 · COMPUTER ARCHITECTURE
Week 4
…the CISC Way
Phase 1 — The ISA · Milestone M1 (microcode)
DUNWOODY
COLLEGE OF TECHNOLOGY

## Slide 2
This Week | Add It in Microcode
You add your instruction the CISC way first — not by changing hardware, but by writing microcode. One layer below the ISA is a tiny program that interprets it.
Concept
The microarchitecture level, Tanenbaum's Mic-1, microprogramming, and the IJVM stack ISA.
Read: SCO 4.1–4.2
Lab · M1
Extend the Mic-1 control store: write the microcode that implements your assigned IJVM instruction, subcycle by subcycle.
Deliverable
Working microcode for your instruction + a trace of its data-path cycles. Reading response #4.
CISC hides complexity in microcode. Next week you'll expose it in hardware — and feel the difference.
D
1

## Slide 3
Where We Are | Two Ways, One Instruction
You understand the datapath. Now add one instruction two different ways so the RISC vs CISC trade-off stops being abstract.
1
DONE · W3
Mapped the datapath; picked the edit points for your instruction.
2
TODAY
Add it the CISC way — microcode on the Mic-1.
3
NEXT · W5
Add it the RISC way — hardware in the core.
4
COMPARE
Same instruction, two microarchitectures. Which was easier? Faster?
Milestone M1's whole point: build the same behavior twice and measure what each style costs.
D
2

## Slide 4
Two Philosophies | CISC vs RISC
Two answers to one question: should the hardware do a lot per instruction, or a little very fast? You'll build both this phase.
CISC — DO MORE PER INSTRUCTION
Rich, variable-length instructions
Interpreted by MICROCODE in hardware
Fewer instructions per program
Complex control, simpler compiler
Examples: x86, IJVM on the Mic-1
RISC — DO LESS, BUT FASTER
Simple, fixed-length instructions
Executed DIRECTLY by hardware
More instructions per program
Simple control, harder-working compiler
Examples: RISC-V, ARM, MIPS
Microcode is the trick that lets simple hardware pretend to be a complex instruction set.
D
3

## Slide 5
The Mic-1 | A Microarchitecture
Tanenbaum's Mic-1 is a minimal datapath driven entirely by microinstructions. Learn its parts — your microcode steers exactly these.
Registers
MAR, MDR, PC, MBR, SP, LV, CPP, TOS, OPC, H — the working set the microcode shuffles data between.
ALU + Shifter
One ALU and a shifter drive the C bus. Every microinstruction can compute one ALU result.
Buses
The B bus feeds the ALU; the C bus writes results back to one or more registers each cycle.
Control Store
The microprogram: 512 words of microcode. MPC selects the next microinstruction.
One ALU, a few buses, and a ROM of microinstructions. That's enough to interpret an entire ISA.
D
4

## Slide 6
Microcode | One Instruction, Many Micro-ops
Each IJVM instruction is not wired in — it's a short microprogram in the control store. Fetch/decode/execute are themselves microcode.
1
Main loop. A microinstruction fetches the next IJVM byte into MBR.
2
Dispatch. The opcode indexes the control store — a multiway microbranch.
3
Execute. Several microinstructions carry out the operation on the datapath.
4
Return. The last micro-op branches back to the main loop for the next byte.
A MICROINSTRUCTION'S FIELDS
NEXT_ADDRESS — where to go next in the store
JAM — conditional microbranch control
ALU / SH — the ALU and shifter function
C — which registers latch the C bus
MEM — read/write/fetch memory this cycle
B — which register drives the B bus
Writing microcode = filling in these fields, one datapath cycle at a time.
D
5

## Slide 7
The Data Path Cycle | Four Subcycles
Every Mic-1 microinstruction runs the datapath through the same four subcycles. Timing is why one micro-op does exactly one ALU operation.
1
SETUP
The chosen register is gated onto the B bus; control signals settle.
2
COMPUTE
The ALU and shifter act on H (A input) and the B bus.
3
WRITE C
The C-bus result latches into the selected registers.
4
NEXT MPC
NEXT_ADDRESS + JAM choose the following microinstruction.
One ALU op per microinstruction — so a rich instruction simply takes more microinstructions.
D
6

## Slide 8
IJVM | A Stack Machine
The Mic-1 interprets IJVM, a subset of the Java Virtual Machine. It's a stack ISA — operands live on a stack, not in named registers.
ILOAD
Push a local variable onto the stack (uses LV + offset).
IADD
Pop two, push their sum. The classic stack operation.
IFEQ
Pop one; branch if it equals zero.
INVOKE
Call a method — the heavy, multi-cycle instruction.
Stack machines make the compiler's job easy and the microcode's job interesting. TOS caches the top.
D
7

## Slide 9
Code-Along | Microcode an Instruction
Here is IADD as microcode, in the MAL notation. Each line is one microinstruction — one datapath cycle.
ijvm.mal
1
// IADD: pop two, push sum
2
iadd1 MAR = SP = SP - 1; rd
3
iadd2 H = TOS
4
iadd3 MDR = TOS = MDR + H; wr;
5
goto Main1
6
7
// your task: microcode ISUB
8
// (hint: reuse H, negate,
9
// then add)
READING THE MICROCODE
SP - 1 walks the stack pointer down
rd / wr issue a memory read / write this cycle
H is the fixed ALU 'A' input — stage operands there
goto Main1 returns to the fetch-decode loop
Each label is one control-store address
Same instruction as next week — but here it's software (microcode), not new wires.
D
8

## Slide 10
Milestone M1 · Lab
Add your instruction in microcode
D
9

## Slide 11
The Lab | Extend the Mic-1
Write and trace the microcode for your assigned IJVM instruction. Same four sections, same rule: explain every microinstruction.
1
ANCHOR
Trace the provided IADD microcode cycle by cycle in the simulator.
2
GUIDED
Write the microcode for a related instruction (e.g. ISUB) together.
3
EXTENSION
Implement your assigned IJVM instruction in the control store.
4
STRETCH
Count its microinstructions; estimate its cycle cost. (Optional.)
Together in class: Anchor + Guided. On your own: Extension + Stretch.
D
10

## Slide 12
Reading Response #4 | SCO 4.1–4.2
Short, specific, in your own words. Post to Canvas before next class.
DEFINE
What is microcode, and where does it live?
What are the fields of a Mic-1 microinstruction?
EXPLAIN
How does the Mic-1 dispatch on an IJVM opcode?
Why does each microinstruction do only one ALU operation?
APPLY
Write the microcode for one simple IJVM instruction.
Count the datapath cycles your assigned instruction needs.
Reference specific registers (H, MDR, SP, TOS) — vague answers about 'the ALU' don't count.
D
11

## Slide 13
Week 4 Reflection | Design Notebook
Log your microcode and its cycle trace. Notebook + check-ins are 8% of your grade.
1
In your own words: what does microcode buy you versus building hardware?
2
Trace it: list the datapath cycles your instruction took, and what each did.
3
Predict: will the hardware (RISC) version next week be faster? Why?
4
One question: which microinstruction field confused you most? Bring it to office hours.
Next week → Add the same instruction the RISC way — real hardware in the core, then compare.
D
12