## Slide 1
COMPUTER ARCHITECTURE · RISC-V: FPGA TO SILICON
Week 4
A Functional Unit from Scratch
DUNWOODY
COLLEGE OF TECHNOLOGY

## Slide 2
Where we left off
Sub-word memory works
lb / lh / lbu / lhu / sb / sh, verified across every offset and both halves.
The warm-up was an ALU op
popcount was one case inside the ALU — a new operation reusing the existing result path.
This week
Build a real functional unit: its own module, its own operands, its own result.
Why it matters
It's the structure Week 5's multicycle multiply will extend with a stall handshake.
D
2

## Slide 3
ALU Op vs Functional Unit
Adding popcount meant one new line inside the ALU. A functional unit is a step up — a block of its own that the datapath feeds and selects.
TWO WAYS TO ADD HARDWARE
An ALU op
A new case inside the ALU. Shares srcA/srcB and the ALU's result wire. Cheap, but limited.
A functional unit
A separate module with its own operands and output, steered into the datapath by a control bit.
Same goal — new behavior — but a unit scales: it can be large, reused, or (next week) multicycle.
WHAT A UNIT NEEDS
1
A module — the logic, written and tested on its own.
2
Operands — routed to the unit from the register file.
3
A select — a control bit that steers its result into writeback.
4
A reference — the golden model computes the same thing.
popcount was an operation; clz will be a unit. The difference is the whole lesson.
D
3

## Slide 4
Anatomy of a Functional Unit
Four parts, and the same four for any unit you ever add to the core.
1
MODULE
Self-contained Verilog: inputs, outputs, internal logic — testable alone.
2
OPERANDS
Tap register values straight into the unit.
3
SELECT
A decoder control bit muxes its result into writeback.
4
VERIFY
Lockstep checks it against an independent reference.
Module, operands, select, verify — learn the pattern once, reuse it for every unit.
D
4

## Slide 5
Count Leading Zeros | clz
Our unit: clz — count the zero bits above the most-significant 1. A real RISC-V Zbb instruction, and a clean from-scratch design.
WHAT clz DOES
Find the top 1
Scan from bit 31 downward to the first set bit.
Count the zeros above
If the highest 1 is at bit k, clz = 31 - k; and clz(0) = 32.
Used for normalization, priority, and fast log2 — small, but real.
EXAMPLES
value (rs1) | clz
0x00000001 | 31
0x00010000 | 15
0x000000FF | 24
0x80000000 | 0
0x00000000 | 32
Five inputs, five answers — the directed test the golden model has to match.
D
5

## Slide 6
clz, Bit by Bit
clz of 0x00010000: fifteen leading zeros, then the first 1 at bit 16. The bits below it don't matter.
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
15 leading zeros
bit 31
bit 0
first 1 at bit 16
clz = 31 - 16 = 15
The unit reports the position of the highest set bit — a priority encoder, in one cycle.
D
6

## Slide 7
Designing the Unit
The hardware is a priority scan: walk from the MSB and stop at the first 1.
THE IDEA
Default to 32
If no bit is set at all, the answer is 32.
Stop at the first 1
Scanning from bit 31 down, the first set bit at index k gives 31 - k.
A priority encoder: the highest set bit wins, everything below it is ignored.
IN VERILOG
1
Start at 32 — assume all zeros.
2
Scan MSB to LSB — loop i from 31 down to 0.
3
First hit wins — on the first set bit, record 31 - i and lock it in.
4
Combinational — it all resolves within one cycle.
No clock, no state — a pure function of the input, like the ALU it sits beside.
D
7

## Slide 8
Wiring It In
The unit lives beside the ALU. Integration is three small touches, plus the module itself.
1
OPERAND
rd1 (the rs1 value) taps straight into the unit.
2
DECODE
custom-0 sets a new control bit, fusel.
3
SELECT
fusel muxes the unit's result into the ALU-result path.
4
NO WIDENING
reuses resultsrc = 0; the writeback mux is untouched.
One new control bit and one mux — the unit slots into the writeback path you already have.
D
8

## Slide 9
Code Along
A module, then three wires
D
9

## Slide 10
RTL | The clz Unit
A standalone module: scan from the top, stop at the first set bit, default to 32.
1
Ports — a 32-bit x in, a 6-bit count out (0..32).
2
Default 32 — covers the all-zeros input.
3
Priority scan — the first set bit from the top wins.
4
Lock with found — later bits can't overwrite the answer.
rv32i.v (clz32)
1
module clz32(input [31:0] x,
2
output reg [5:0] cnt);
3
cnt = 6'd32; found = 0;
4
for (i=31; i>=0; i=i-1)
5
if (!found && x[i]) begin
6
cnt = 31 - i;
7
found = 1; end
8
endmodule
IDEA
highest set bit -> 31 - index
It's a function of x alone — testable on its own, before it ever touches the core.
D
10

## Slide 11
RTL | Wiring It In
Tap rd1 into the unit, then let one decoder bit select its result into writeback.
1
Decode — custom-0 sets fusel = 1 and regwrite = 1.
2
Instantiate — clz32 reads rd1 directly.
3
Select — fusel ? clz result : ALU result.
4
Writeback — feeds the existing resultsrc = 0 path.
rv32i.v wiring
1
// main_decoder
2
7'b0001011: begin
3
regwrite=1; fusel=1; end
4
// datapath
5
clz32 CLZ (.x(rd1),
6
.cnt(clz_count));
7
wire [31:0] alumux = fusel ?
8
{26'd0,clz_count} : aluresult;
ASSEMBLED
clz x2, x1 -> 0x0000910b
fusel is the whole integration: it picks the unit over the ALU on the shared writeback path.
D
11

## Slide 12
Model + Assembler
Teach the golden model the same answer and the assembler the mnemonic — then lockstep covers it.
1
Model it — 32 - x.bit_length() gives 32 for zero, free.
2
Add the mnemonic — clz rd, rs1 in the assembler.
3
Custom-0 — opcode 0x0B, funct3 001.
4
Nothing else — the harness already compares the writeback.
rv32i_iss.py + asm.py
1
# golden model
2
elif op == 0x0B:
3
wb(32 - a.bit_length())
4
# assembler
5
if op == "clz": out.append(
6
enc_i(reg(args[0]), reg(args[1]),
7
0, 0x1, op=0x0B))
TERMINAL
model + assembler in step
32 - x.bit_length() is the oracle; lockstep enforces the hardware agrees with it.
D
12

## Slide 13
Run Lockstep | Edges and Extremes
Directed inputs — one, the extremes, and zero — each checked against the model.
1
Pick edges — 1, 0x80000000, 0x10000, 255, 0, 16.
2
Assemble — make prog builds the hex image.
3
Run lockstep — make sim steps the core and model together.
4
Read PASS — 15 instructions, all matched.
clz_test.s
1
clz x2, x1 # clz(1) = 31
2
clz x4, x3 # 0x80000000 = 0
3
clz x6, x5 # 0x00010000 = 15
4
clz x8, x7 # 255 = 24
5
clz x12, x9 # 0 = 32
6
clz x14, x13 # 16 = 27
TERMINAL
$ make prog && make sim
lockstep OK: 15 matched
** test_lockstep PASS
Validated: 15 instructions, every clz boundary, RTL and model in lockstep — PASS.
D
13

## Slide 14
Module → Route → Select → Verify
A functional unit added end-to-end, by the same four steps you'll reuse for every unit.
1
MODULE
clz32 — a from-scratch priority encoder, testable on its own.
2
ROUTE
rd1 taps straight into the unit's input.
3
SELECT
fusel muxes its result onto the writeback path.
4
VERIFY
lockstep against 32 - x.bit_length().
Next: the multicycle multiply — the same separate-unit pattern, but it can't finish in one cycle, so it needs a done/stall handshake. That's where single-cycle finally breaks.
D
14