## Slide 1
CENG 4100 · COMPUTER ARCHITECTURE
Week 5
…the RISC Way
Phase 1 — The ISA · Milestone M1 completes
DUNWOODY
COLLEGE OF TECHNOLOGY

## Slide 2
This Week | Add It in Hardware
Now the real thing: no microcode interpreter, just wires. You'll add your instruction directly to the RISC core and then weigh it against the CISC version.
Concept
The RISC-V ISA in depth: encoding, decode, immediate generation, ALU control, register conventions.
Read: COD 2.1–2.10, 2.16–2.18; SCO 4.3–4.5
Lab · M1
Add your instruction to the RISC core: extend decode, imm-gen, ALU control, and the datapath. Verify it in hardware.
Deliverable
Your instruction running on the core + a written RISC-vs-CISC comparison. Reading response #5.
Two builds, one instruction. This is where the trade-off becomes something you've felt with your hands.
D
1

## Slide 3
Where We Are | The Second Build
You added your instruction in microcode last week. Today you add the same instruction in hardware — and finish Milestone M1.
1
DONE · W4
Instruction working as Mic-1 microcode; cycle cost measured.
2
TODAY
Add it as real hardware in the RISC core; verify on the board.
3
COMPARE
Design effort, cycle count, and Fmax impact — CISC vs RISC.
4
NEXT · P2
Beef up the ALU: full arithmetic and RV32M multiply/divide.
Finish M1 today: same instruction, two microarchitectures, one honest comparison.
D
2

## Slide 4
The RISC-V ISA | 32 Registers, One Rule
RV32I is deliberately small and regular. Thirty-two 32-bit registers, a fixed 32-bit instruction, and a calling convention everyone agrees on.
x0
Hard-wired to zero. Reads as 0, writes are discarded — the source of many clever idioms.
ra, sp
x1 is the return address; x2 is the stack pointer. The ABI reserves them by convention.
a0–a7
Argument and return registers (x10–x17). How functions pass values.
t / s regs
Temporaries (caller-saved) and saved registers (callee-saved). The compiler juggles these.
Regularity is the point: every instruction is 32 bits, and rd / rs1 / rs2 always sit in the same fields.
D
3

## Slide 5
Encoding | Where the Fields Live
Because the fields are fixed, decode is just slicing bits. Here's an R-type and an I-type, side by side in Verilog.
decode.v
1
wire [6:0] opcode = instr[6:0];
2
wire [4:0] rd = instr[11:7];
3
wire [2:0] funct3 = instr[14:12];
4
wire [4:0] rs1 = instr[19:15];
5
wire [4:0] rs2 = instr[24:20];
6
wire [6:0] funct7 = instr[31:25];
7
// I-type immediate (sign-ext)
8
wire [31:0] immI =
9
{{20{instr[31]}}, instr[31:20]};
FIXED FIELDS PAY OFF
rs1, rs2, rd are ALWAYS in the same bits
So the register file can read before decode finishes
funct3 + funct7 select the exact ALU operation
opcode picks the format and the control signals
Fixed-field encoding is why RISC decode is cheap — no microcode ROM required.
D
4

## Slide 6
The Four Edits | Where You'll Cut
Adding an instruction to the hardware touches at most four places. Know them before you open the file.
1
DECODE
Add a case for your opcode/funct; assert its control signals.
2
IMM-GEN
If it uses an immediate, extend the generator for its format.
3
ALU CTRL
Map funct3/funct7 to a new ALU operation if needed.
4
DATAPATH
Route any new operand or result path and its write-back.
Contrast last week: no control store, no dispatch — just four targeted RTL edits.
D
5

## Slide 7
Immediates | Sign-Extend by Format
The immediate is scattered across the instruction differently in each format. Imm-gen reassembles and sign-extends it to 32 bits.
immgen.v
1
always @(*) case (fmt)
2
I: imm = {{20{instr[31]}},
3
instr[31:20]};
4
S: imm = {{20{instr[31]}},
5
instr[31:25],
6
instr[11:7]};
7
B: imm = {{19{instr[31]}}, ...};
8
endcase
WHY IT'S FIDDLY
S and B split the immediate across two fields
B and J drop the low bit (targets are even)
The top bit is always the sign — replicate it
Get the bit ranges wrong → silent wrong branches
RISC-V scrambled the immediate on purpose — to keep rs1/rs2/rd bits fixed. Imm-gen pays that bill.
D
6

## Slide 8
Code-Along | Add the Instruction
Teach the ALU-control block one new operation, then wire it into decode. This is the whole hardware edit for a reg-reg instruction.
alu_ctrl.v
1
// add a new R-type op: e.g. min
2
always @(*) case ({funct7,funct3})
3
10'b0000000_000: alu_op = ADD;
4
10'b0100000_000: alu_op = SUB;
5
10'b0000000_100: alu_op = XOR;
6
// your new op below:
7
10'b0000001_110: alu_op = MIN;
8
default: alu_op = ADD;
9
endcase
VERIFY
$ xsim tb_core
PASS: add x3 = 7
PASS: sub x4 = 1
PASS: min x5 = 3 <-- new
$ report_timing_summary
WNS: 1.05 ns (still met)
$ program device
INFO: min runs on board
One case arm + one ALU op = a new instruction. No ROM, no dispatch — that's the RISC promise.
D
7

## Slide 9
The Trade-Off | What You Just Felt
You built the same instruction twice. Now put the two experiences side by side — this comparison is part of your deliverable.
CISC (MICROCODE)
Edit software in the control store
No new wires or timing risk
Costs several datapath cycles
Adds latency, not area
RISC (HARDWARE)
Edit the RTL — real logic
May lengthen the critical path
Executes in one cycle
Adds area, not cycles
Neither wins outright. CISC trades cycles for simplicity; RISC trades area and timing for speed.
D
8

## Slide 10
Milestone M1 · Lab
Add your instruction in hardware
D
9

## Slide 11
The Lab | Cut Into the Core
Add your assigned instruction to the RISC core and verify it on the board. Same four sections, same rule: explain every edit.
1
ANCHOR
Add a provided reg-reg op to ALU control; simulate it passing.
2
GUIDED
Wire that op through decode and verify in the testbench together.
3
EXTENSION
Implement your assigned instruction fully; program it to the board.
4
STRETCH
Check Fmax impact; write the RISC-vs-CISC comparison. (Optional.)
Together in class: Anchor + Guided. On your own: Extension + Stretch.
D
10

## Slide 12
Reading Response #5 | COD 2.1–2.10
Short, specific, in your own words. Post to Canvas before next class.
DEFINE
Which instruction bits hold rs1, rs2, and rd?
What does imm-gen do, and why is it format-dependent?
EXPLAIN
Why does fixed-field encoding speed up decode?
How does ALU control use funct3 and funct7?
APPLY
List the four RTL edits your instruction needed.
Compare its cycle cost to last week's microcode version.
Point to real bit ranges and signal names. This is a hardware answer, not a paraphrase.
D
11

## Slide 13
Week 5 Reflection | Design Notebook
Log both builds and your verdict. Notebook + check-ins are 8% of your grade.
1
In your own words: why is RISC decode cheaper than CISC dispatch?
2
Compare: which build was harder, and which instruction ran faster?
3
Measure: did adding the instruction change your core's Fmax? By how much?
4
One question: which of the four edits was trickiest? Bring it to office hours.
Next week → Arithmetic: extend the ALU and add an RV32M multiply/divide unit.
D
12