## Slide 1
CENG 4100 · COMPUTER ARCHITECTURE
Week 6
Arithmetic
Phase 2 — Arithmetic · Milestone M2
DUNWOODY
COLLEGE OF TECHNOLOGY

## Slide 2
This Week | Teach It to Compute
Your core can move data and branch — now make it do real math. You'll grow the ALU and drop in a multiply/divide unit, then meet floating point.
Concept
Number representation, ALU design, fast adders, and the RV32M multiply/divide algorithms; FP overview.
Read: COD 3.1–3.6, 3.9
Lab · M2
Extend the ALU (add/sub, logic, shifts, compares) and add an RV32M mul/div unit. Verify each new op on the board.
Deliverable
An ALU that passes the arithmetic test suite + mul/div working. Reading response #6. (Midterm is next week.)
Note: the midterm in Week 7 covers Weeks 1–6. This week's math is fair game.
D
1

## Slide 3
Where We Are | Phase 2 Begins
Phase 1 is done — you added instructions two ways. Phase 2 is about the datapath's math engine: the ALU and the multiplier.
1
DONE · P1
Instruction added in microcode and in hardware; M1 complete.
2
TODAY
Extend the ALU; add RV32M multiply and divide; FP overview.
3
NEXT · W7
Midterm (covers Weeks 1–6), then: why single-cycle is slow.
4
THEN · P3
Pipeline the whole core into five stages.
Milestone M2 = a core that can add, shift, compare, multiply, and divide — and prove it on hardware.
D
2

## Slide 4
Representation | Bits Into Numbers
Before you build arithmetic, agree on what the bits mean. Two's complement is why one adder handles both add and subtract.
Unsigned
0 … 2ⁿ−1. Plain binary place value. Used for addresses and counts.
Two's Comp.
Signed: the top bit has weight −2ⁿ⁻¹. Negation = invert then add 1.
Sub = Add
a − b = a + (~b + 1). One adder does both — just invert b and set carry-in.
Overflow
Signed overflow when the carry into and out of the sign bit differ. Flag it.
Two's complement is the reason your ALU needs only an adder, not a separate subtractor.
D
3

## Slide 5
Building the ALU | One Block, Many Ops
The ALU is a mux over parallel operators: all of them compute, and alu_op selects which result comes out.
alu.v
1
always @(*) case (alu_op)
2
ADD: y = a + b;
3
SUB: y = a - b;
4
AND: y = a & b;
5
OR : y = a | b;
6
XOR: y = a ^ b;
7
SLL: y = a << b[4:0];
8
SRL: y = a >> b[4:0];
9
SLT: y = ($signed(a) <
10
$signed(b));
11
endcase
DESIGN NOTES
Every arm computes in parallel; the case is a mux
Shift amount is only the low 5 bits (0–31)
SLT needs $signed for the comparison to be correct
Keep the ALU purely combinational — it's on the critical path
Add operations by adding case arms. But every arm you add can lengthen the critical path — watch Fmax.
D
4

## Slide 6
Adders | Ripple vs Look-Ahead
The adder often sets the ALU's speed. A ripple-carry adder is tiny but slow; carry-lookahead trades area for a shorter carry path.
RIPPLE-CARRY
Carry chains through all n bits
Delay grows linearly, O(n)
Smallest area
Fine for narrow or non-critical adds
CARRY-LOOKAHEAD
Computes carries in parallel with generate/propagate
Delay ~O(log n)
More logic (LUTs)
Use when the adder limits Fmax
On the Artix-7, the fabric has fast carry chains — measure before you hand-build a lookahead adder.
D
5

## Slide 7
Multiply | RV32M · shift-and-add
Multiplication is repeated shift-and-add. The classic algorithm walks the multiplier bit by bit; Booth's recoding cuts the work.
1
INIT
Product = 0. Load multiplicand and multiplier into registers.
2
TEST BIT
If the low multiplier bit is 1, add the multiplicand to the product.
3
SHIFT
Shift the multiplicand left (or product right) one position.
4
REPEAT
32 iterations for RV32. Booth recoding handles runs of 1s faster.
On the Artix-7 you can instead infer a DSP48 multiplier — one line of Verilog, one hardened block.
D
6

## Slide 8
Divide | RV32M · restoring
Division is repeated subtract-and-shift. Restoring division subtracts, and puts the value back when it goes negative.
1
SHIFT
Shift the remainder left, bringing in the next dividend bit.
2
SUBTRACT
Subtract the divisor from the remainder.
3
TEST
If negative, restore (add divisor back), quotient bit = 0; else bit = 1.
4
REPEAT
32 iterations. Handle divide-by-zero per the RV32M spec.
Multiply and divide are multi-cycle — the first place your core's CPI rises above 1. Note that for Week 7.
D
7

## Slide 9
Code-Along | Drop In the Multiplier
For RV32M you can let the tools infer a DSP-based multiplier, then wrap a small FSM around a divider. Here's the multiply path.
muldiv.v
1
// RV32M: mul (low 32 bits)
2
wire [63:0] prod =
3
$signed(a) * $signed(b);
4
assign mul_y = prod[31:0];
5
6
// mulh: high 32 bits
7
assign mulh_y = prod[63:32];
8
// div/rem: multi-cycle FSM
9
// asserts busy until done
VERIFY
$ xsim tb_muldiv
PASS: mul 6*7 = 42
PASS: mulh hi bits ok
PASS: div 20/3 = 6
PASS: rem 20%3 = 2
$ report_utilization | grep DSP
DSPs: 4 / 90 <-- inferred
$ program device
The * operator infers a DSP48; divide needs an FSM and raises CPI. Both are real trade-offs to record.
D
8

## Slide 10
Floating Point | IEEE 754 Overview
You won't build an FPU this phase, but you must read numbers in IEEE 754. A float is three fields that encode sign, scale, and precision.
Sign · 1 bit
0 = positive, 1 = negative. Simple.
Exponent · 8 bits
Biased by 127. Sets the scale (the binary point's position).
Fraction · 23 bits
The mantissa, with an implicit leading 1. Sets precision.
value = (−1)ˢ × 1.fraction × 2^(exp − 127). Precision is finite — never test floats with ==.
D
9

## Slide 11
Milestone M2 · Lab
Extend the ALU; add mul / div
D
10

## Slide 12
The Lab | Grow the Math Engine
Extend the ALU and add RV32M multiply/divide, verifying each op. Same four sections, same rule: explain every result.
1
ANCHOR
Add the logic and shift ops to the ALU; pass the provided tests.
2
GUIDED
Add SLT/SLTU and overflow detection together; verify signed compares.
3
EXTENSION
Add RV32M mul (DSP-inferred) and a multi-cycle div FSM.
4
STRETCH
Measure the Fmax and DSP-utilization cost of mul/div. (Optional.)
Together in class: Anchor + Guided. On your own: Extension + Stretch.
D
11

## Slide 13
Reading Response #6 | COD 3.1–3.6, 3.9
Short, specific, in your own words. Post to Canvas before next class.
DEFINE
How does two's complement turn subtraction into addition?
Name the three fields of an IEEE 754 single.
EXPLAIN
Why is carry the bottleneck in a ripple adder?
Why do multiply and divide push CPI above 1?
APPLY
Decode a given 32-bit float to its value.
Report the DSP/Fmax cost of your multiplier.
Show your bit-level work. 'The ALU multiplies' is not an answer about how.
D
12

## Slide 14
Week 6 Reflection | Design Notebook
Log your ALU ops and the mul/div costs. Notebook + check-ins are 8% of your grade.
1
In your own words: why does one adder suffice for both add and subtract?
2
Measure: what did mul/div cost you in DSPs, Fmax, and CPI?
3
Prep the midterm: list the Week 1–6 topics you're least sure of.
4
One question: restoring division or Booth — which still confuses you? Office hours.
Next week → Midterm (Weeks 1–6), then Phase 3: why single-cycle is slow, and the 5-stage plan.
D
13