## Slide 1
COMPUTER ARCHITECTURE · RISC-V: FPGA TO SILICON
Week 1
Toolchain & Your First Working CPU
DUNWOODY
COLLEGE OF TECHNOLOGY

## Slide 2
Course Outcomes (for your resume)
RISC-V Microprocessor: FPGA Prototype to Custom Silicon (Aug 2026 – Dec 2026)
Verilog · Xilinx Vivado · Verilator · cocotb · Yosys · OpenROAD · LibreLane · Magic · KLayout · SKY130 PDK · Tiny Tapeout · Basys 3 (Artix-7)
Designed and verified a single-cycle RV32I processor in Verilog, extending its instruction set and running it on a Basys 3 (Artix-7) FPGA.
Built a lockstep verification harness comparing the RTL core against a golden ISA model, with differential testing for every added instruction.
Hardened an area-optimized variant to GDSII using the open-source RTL-to-GDS flow (Yosys, OpenROAD, LibreLane) on the SKY130 process.
Submitted the design to a Tiny Tapeout multi-project shuttle for fabrication as a real ASIC.
D
2

## Slide 3
What to expect each week
FPGA First
Every week we build and test on the Basys 3 — fast feedback on real hardware before anything touches silicon.
The Core You Extend
Start from a small, working RV32I core. Each week you add an instruction that teaches a new piece of the machine.
Verify Everything
A golden-model lockstep harness gates every change. If it isn't verified against the reference, it isn't done.
Then Silicon
The final weeks harden your core to GDSII with the open ASIC flow and submit it to a real Tiny Tapeout shuttle.
D
3

## Slide 4
Let’s Get Set Up
Vivado · Verilator · cocotb · and the open-source ASIC flow
D
4

## Slide 5
Set Up Your Flows | FPGA + ASIC
Two toolchains, two jobs. The FPGA flow gives fast iteration on real hardware; the open-source ASIC flow turns the same Verilog into a manufacturable chip.
TWO FLOWS, TWO JOBS
Vivado — the FPGA flow
Compiles your Verilog to a bitstream for the Basys 3 in minutes. This is where you design and debug.
Open ASIC tools — the silicon flow
Turn the same Verilog into a chip layout for a foundry. Slower and exact — this is the final artifact.
Same Verilog, two destinations. You design on the FPGA and ship to silicon.
TODAY’S STEPS
1
Install Vivado — the free Standard edition supports the Basys 3’s Artix-7 (XC7A35T).
2
Add simulators — Verilator and Icarus Verilog for fast RTL simulation.
3
Add cocotb — pip install cocotb — Python testbenches, the style Tiny Tapeout uses.
4
Get the RISC-V toolchain — riscv64-unknown-elf-gcc, to assemble test programs.
Install once this week — after this, you just open the project and build.
D
5

## Slide 6
The Open ASIC Flow | RTL to GDSII
No license, no fees: a chain of open-source tools takes your Verilog all the way to a fabrication-ready layout.
THE TOOLCHAIN
Synthesis & layout
Yosys turns RTL into gates; OpenROAD places and routes them; LibreLane orchestrates the whole flow.
Layout & signoff
Magic and KLayout view and check the layout; Netgen confirms it matches the netlist (DRC / LVS).
LibreLane runs the whole chain for you — you read its reports and iterate.
TODAY’S STEPS
1
Install the flow — Yosys, OpenROAD, and LibreLane (the FOSSi successor to OpenLane).
2
Add the PDK — fetch SKY130 with the ciel / volare manager.
3
Add layout tools — Magic, KLayout, and Netgen for DRC and LVS.
4
Clone the template — Tiny Tapeout’s ttsky-verilog-template ships the CI that hardens your design.
efabless closed in 2025 — this is the free community flow that replaced it.
D
6

## Slide 7
Code Along
Run a CPU you didn’t write — yet
D
7

## Slide 8
How RTL Becomes Hardware
The same Verilog follows one path to an FPGA and another to an ASIC. Both start the same way.
1
WRITE RTL
Describe the hardware in Verilog — modules, registers, logic. One source for both targets.
2
SIMULATE
Run it in software (Verilator / cocotb) and check behavior before any hardware exists.
3
SYNTHESIZE
Vivado maps it to FPGA LUTs; Yosys maps it to standard cells for the ASIC.
4
BUILD
Out comes a Basys 3 bitstream — or a GDSII layout ready for the foundry.
Simulation is where you find bugs cheaply. Always simulate before you build.
D
8

## Slide 9
Run the Base Core | On the Basys 3
Prove your FPGA flow works by running the provided RV32I core on real hardware.
1
Open the project — launch Vivado and open the base core with its Basys 3 constraints.
2
Generate the bitstream — run synthesis, implementation, and bitstream generation.
3
Program the board — connect the Basys 3 over USB and download the bitstream.
4
Read the result — the core runs a tiny program; its output appears on the LEDs.
BASYS 3 · led[7:0]
0b0000 1111 = 0x0F = 15
Bitstream on the board, LEDs showing 15 (5 + 10). Your FPGA flow works.
D
9

## Slide 10
Prove It in Simulation | cocotb
Hardware is slow to re-flash; simulation is instant. Run the same core under cocotb and check its output in software.
1
Go to the test folder — cd test, where the cocotb harness lives.
2
Run the test — make sim builds the core and runs the Python testbench.
3
Check automatically — the test runs a program and asserts the result — no eyeballing.
4
Read PASS — a green result means the core behaves exactly as expected.
test_cpu.py
1
make sim
2
smoke: program 5 + 10
3
assert cpu_out == 15
TERMINAL
PASS: cpu_out = 15
** test_cpu.smoke PASS
** TESTS=1 PASS=1 FAIL=0
Self-checking tests are the foundation of everything you do in Week 2.
D
10

## Slide 11
Smoke-Test the ASIC Flow | Counter → GDS
Don’t wait until the final weeks to discover a broken ASIC install. Push a trivial design all the way to a chip layout today.
1
Take a trivial design — a simple counter, small enough to harden in minutes.
2
Run LibreLane — it synthesizes, places, routes, and checks the design.
3
Get a GDSII — the same file format that goes to the foundry.
4
Confirm clean — DRC and LVS pass on the toy design.
librelane
1
librelane config.json
2
target: sky130
TERMINAL
[synthesis] ok
[place/route] ok
[DRC] clean
[LVS] clean
-> counter.gds
If the flow works on a counter today, it’ll work on your CPU later — with slack to spare.
D
11

## Slide 12
This Week’s Loop
You installed both flows, ran a working CPU on the board, and proved each toolchain end-to-end.
1
WRITE
One Verilog source, targeting both the FPGA and the ASIC.
2
SIMULATE
cocotb checks behavior in software — instant feedback, self-checking.
3
BUILD
A bitstream on the Basys 3, and a GDS proving the ASIC flow works.
Next week: stop trusting the core — trace it, prove you understand it, then extend it.
D
12